## Slide 1: Structural Heart Live Cases
Supported by:
Edwards Lifesciences
Bard Inc
Terumo Medical Corp

## Slide 2: Disclosures
Samin K. Sharma, MD, FACC
Speaker’s Bureau – Boston Scientific Corp., Abbott Vascular Inc, ABIOMED, CSI
Annapoorna S. Kini, MD, FACC
Nothing to disclose
Farzan Filsoufi, MD, CT Surgeon
Nothing to disclose
Gilbert Tang, MD: Moderator
Physician proctor for Edwards Lifesciences

## Slide 3: March 12th 2019- Structural Heart Live Case #28: KS, 79 yo M
Presentation: Severe dyspnea on exertion NYHA Class III x 3 months
PMH: Bentall procedure (2011) with 25 mm Carpentier-Edwards pericardial valve (Perimount 2700) inside 30 mm Hemashield tube for symptomatic bicuspid aortic stenosis and dilated ascending aorta, Atrial Fibrillation, Hypertension, Dyslipidemia
Medications: Warfarin, Digoxin, Carvedilol, Simvastatin, Furosemide, Pantoprazole, Doxepin, Lisinopril
Labs: Hgb 10.1, PLT 275, K 4.7, Cr 1.1, INR 1.9
EKG (3/04/19): AF, LBBB
Cath (12/31/18): Non-obstructive coronaries
TEE (01/10/19): EF 35%, moderate to severe trans-valvular aortic regurgitation with degenerative leaflets, mild MR, mild TR, possible small thrombus in LAA

## Slide 4: Trans-Esophageal Echo (TEE)
Severe trans-valvular AR with eccentric jet
Severe trans-valvular AR

## Slide 5
Aortic Annulus
Max: 25.7 mm
Min: 22.1 mm
Mean: 23.9 mm
Perimeter = 76 mm
Area = 454.8 mm2
LVOT
Max: 25.6 mm
Min: 31.1 mm
Mean: 28.3 mm
Perimeter = 88.9 mm
Area = 611 mm2
CTA: Aortic Annulus and LVOT
Annulus and LVOT
Annulus: 22.1x25.7 mm
Area: 454.8 mm2 Perimeter: 76 mm
LVOT: 25.6X31.1 mm
Area: 611 mm2 Perimeter: 88.9 mm

## Slide 6
CTA: SOV, VTC
RCC: 33.3 mm
LCC: 35 mm
NCC: 32 mm
Sinus of Valsalva
RCC = 33.3 mm
LCC = 35 mm
NCC = 32 mm
Virtual THV-coronary (VTC) distance
VTC = 7.0 mm
VTC: 7.0 mm
26 mm THV

## Slide 7
Coronary heights
LCA = 16.5 mm
RCA = 25.5 mm
STJ height (above annulus) = 32 mm
STJ = 31.7 x 32.8 mm (mean 31.8)
Root angle = 43 deg
Ascending aorta = 33 x 32.1 mm
CTA: STJ, Coronary Ostia
STJ: 31.7x32.8 mm
LCA: 16.5mm
RCA: 25.5mm
Root angle: 43 deg

## Slide 8: Femoral Arterial Access
Longitudinal View RFA and RIA
Access 3D
7.8x9.1
7.5x8.8
8.1x8.6
8.3x7.5
10x11.6
9.4x11.4
Longitudinal View LFA and LIA

## Slide 9
LAO: 40°
Caudal: 0°
RAO: 30°
Caudal: 10°
Great Vessel Anatomy for Cerebral Protection Device

## Slide 10: Sapien-3 Valve selection of ViV TAVR

## Slide 11: Biometrics and Indexed Effective Orifice area (iEOA) to predict PPM
Biometrics
Height = 180 cm
Weight = 87.1 Kg
BMI = 26.88 Kg/m²
BSA = 2.07 m²
iEOA (calculated) for 26 mm Sapien-3 Valve
In-Vitro iEOA = 1.1 cm²/m²
In-Vivo iEOA = 0.82 cm²/m²
Hahn RT et al. JACC Cardiovasc Imaging. 2019;12(1):25.

## Slide 12
Valve-in-Valve TAVR vs Native Valve TAVR for AS
Tuzcu et al., J Am Coll Cardiol 2018;72:370

## Slide 13
Mean Gradients at Baseline and Discharge
ViV-TAVR by Transcatheter Heart Valve (THV) Type
Tuzcu et al., J Am Coll Cardiol 2018;72:370

## Slide 14
Presentation: 79 year old male with NYHA Class III DOE and HF admissions
TTE: EF 35%, severe trans-valvular aortic regurgitation due to degenerative bio-prosthetic leaflets
STS risk mortality: 8.3 %
EuroScore II risk: 6.10%
Logistic Euroscore mortality: 19.37%
Course: Patient was evaluated by Heart Team and due to co-morbidities and frailty status, the patient was determined to be High Risk for reop SAVR.
Plan: The patient is referred here for Valve-in-Valve TAVR with 26 mm Sapien-3 Valve +/- bio-prosthetic valve fracture technique via left percutaneous femoral approach with Sentinel cerebral protection device.
Summary of Case

## Slide 15: Issues Related To The Case
TAVR vs SAVR valve durability
Bio-prosthetic Valve Fracture (BVF)

## Slide 16
General Classification of Bioprosthetic Valves
Rodriguez-Gabella et al., J Am Coll Cardiol 2017;70:1013

## Slide 17
Structural Valve Degeneration Following Surgical
or Transcatheter Aortic Bio-prosthesis Implantation
Aortic Bioprosthetic Valve Replacement
Surgical/
Transcatheter
Younger Age
Cardiovascular Risk Factors
Bioprosthetic Valve-Related Factors
Valve Calcification/ Leaflet Degradation
Valve Stenosis and/or Regurgitation
Clinically Relevant Structural Valve Degeneration
(<15% at 10 Years Post-SAVR)
Redo
Surgery
Valve-in-Valve
TAVR

## Slide 18
Definitions of Structural Valve Degeneration

## Slide 19
CoreValve 5-Yr F/U
Rodriguez-Gabella et al., J Am Coll Cardiol 2017;70:1013
Echo evaluation
Rodriguez-Gabella et al., J Am Coll Cardiol 2017;70:1013
Echo Evaluation
Partner 5-Yr F/U

## Slide 20
Defined as Mean Gradient of ≥20 mmHg and an Increase in Mean Gradient ≥10 mmHg After 3 Months Post-Procedure

## Slide 21
NOTION Trial: Mean Gradient and Effective Orifice
Area of Transcatheter and Surgical Bioprosthetic Aortic Valves Annually Through 6 Years
Søndergaard et al., J Am Coll Cardiol 2019;73:546

## Slide 22
NOTION Trial: Cumulative Incidence of Structural Valve Deterioration Through 6 Years
Søndergaard et al., J Am Coll Cardiol 2019;73:546
The cumulative incidence of SVD was significantly lower after TAVR compared with SAVR through 6 years follow-up
Defined as Mean Gradient of ≥20 mmHg and an Increase in Mean Gradient ≥10 mmHg After 3 Months Post-Procedure

## Slide 23
NOTION Trial: Structural Valve Deterioration and
Its Components Through 6 Years
Søndergaard et al., J Am Coll Cardiol 2019;73:546
*The 3-month echo measurements are the first post-procedure measurements in NOTION

## Slide 24
NOTION Trial: Cumulative Incidence of SVD
Søndergaard et al., J Am Coll Cardiol 2019;73:546
Rate of SVD by this definition is lower for SAVR but remains significantly greater than the SVD rate for TAVR through 6 years
Defined as Mean Gradient of ≥20 mmHg and an Increase in Mean Gradient ≥10 mmHg After 3 Months Post-Procedure

## Slide 25
NOTION Trial: Cumulative Incidence of
Bioprosthetic Valve Failure Through 6 Years
Søndergaard et al., J Am Coll Cardiol 2019;73:546
No significant difference in BVF between TAVR and SAVR through 6 years

## Slide 26
NOTION Trial: Aortic Valve Durability at 6 Years
Søndergaard et al., J Am Coll Cardiol 2019;73:546
Chart: 
| Valve failure | Valve dysfunction
SAVR (n=135) | 6.7 | 24
TAVR (n=139) | 7.5 | 4.8
%

## Slide 28
The PARTNER 3 Trial
1:1 Randomization (n=1228)
TF - TAVR
(SAPIEN 3)
Surgery
(Bioprosthetic Valve)
Follow-up: 30 days, 6 mos, 1 year and annually through 10 years
CT Imaging Sub-Study (n=200)
Low Risk ASSESSMENT by Heart Team
(STS < 3%, TF only)
Symptomatic Severe Calcific AS
Primary Endpoint:
Composite of all-cause mortality, all strokes, or re-hospitalization at 1 year
CT Imaging Sub-Study (n=200)
Results in ACC 2019
QOL Data
Evolut Low Risk Trial
Primary Endpoint:
Composite of all-cause mortality and strokes at 2 year

## Slide 30
Bioprosthetic Surgical Valves
Dvir et al., Circ J 2015;79:695
A. Common Bioprosthetic Surgical Valves
B. Fluoroscopic Images of Common Stented Bioprosthetic Valves
Perimount Mosaic Mitroflow Carpentier-Edwards
Epic Trifecta Hancock II Freestyle

## Slide 31
Analysis of Post-Procedure Gradients After VIV Procedures According to Surgical Bioprosthesis Size
Dvir et al., Circ J 2015;79:695
Small (internal diameter <20 mm), Intermediate (≥20 mm and <23 mm) and Large (≥23 mm)

## Slide 32
Echocardiographic Outcomes
Tuzcu et al., J Am Coll Cardiol 2018;72:370

## Slide 34
Summary of Bench Testing in High Pressure
Balloon Inflation to Fracture the Valve Frame of Surgical Tissue Valves
Allen et al., Ann Thorac Surg 2017;104:1501

## Slide 35
Bio-prosthetic Valve Fracture after Sapien XT 20mm

## Slide 37
Ex Vivo Bench Testing Methodology
Sathananthan et al., J Am Coll Cardiol Intv 2019;12:65
Micro CT used to scan THVs
Micro CT image of Sapien 3 THV (arrows indicate measurement made at inflow, middle and outflow of valve)
ACURATE neo THV (arrows indicate measurements made at inflow, leaflet nadir, and leaflet coaptation level of the valve)
Pulse duplicator used for hydrodynamic testing
THV silicon holder
Mid-strut measurements of THV

## Slide 38
Ex Vivo Bench Study: Multimodality Imaging
Pre- and Post-BVF
Sathananthan et al., J Am Coll Cardiol Intv 2019;12:65

## Slide 39
Ex Vivo Bench Study: Hydrodynamic Function at Baseline Following VIV TAVR and With Sequential Post-Dilatation and BVF
Sathananthan et al., J Am Coll Cardiol Intv 2019;12:65

## Slide 40
Ex Vivo Bench Study: Pin-Wheeling Index (%)
Pre- and Post-Fracture
Sathananthan et al., J Am Coll Cardiol Intv 2019;12:65
Pin-wheeling, as defined by the International Standards Organization guideline for THV testing, refers to twisting of the leaflet redundancy.

## Slide 42
Take Home Messages for TAVR vs SAVR valve durability and Valve fracture technique
First RCT data on comparative outcomes of valve durability at 6yrs have shown lower structural valve deterioration with TAVR valve vs SAVR valve. Overall valve failure (degeneration) rate is 5-7% at 6yrs and is similar between 2 approaches. These data are very reassuring when we start implanting TAVR in younger lower risk AS patients.
Selected degenerated bio-prosthetic valves can safely undergo valve fracture technique to reduce residual gradient at the time of TAVR implantation (before or after TAVR). Long-term results on the TAVR valve durability are awaited after valve fracture technique.

## Slide 43: Question # 1
Following is the true statement regarding comparative long-term durability of TAVR vs SAVR valve:
  TAVR valve has lower structural valve deterioration
  SAVR valve has lower structural valve deterioration
  TAVR valve has lower valve failure
  SAVR valve has lower valve failure
Correct answer: A

## Slide 44: Question # 2
Following is the incidence of aortic valve failure/degenaration after TAVR/SAVR in the NOTION trial at 6yrs :
  <5%
  6-8%
  9-10%
  >10%
Correct answer: B

## Slide 45: Question # 3
Following are the true statements regarding bio-prosthetic valve fracture (BVF) technique except:
  A. BVF cause significant decrease in the residual gradient
  B. BVF can be done with all types of bio-SAVR
  C. BVF is associated with low complication rates
  D. BVF usually does not cause injury to the TAVR valve
Correct answer: B