## Slide 1: Structural Heart Live Cases
Supported by:
Medtronic Inc.
Abbott Inc.
Bard Inc.
Cook Inc.

## Slide 2: Faculty Involved and Disclosures
Samin K. Sharma, MD, FACC, MSCAI
Speaker’s Bureau – BSC
Annapoorna S. Kini, MD, FACC
Nothing to disclose
Sahil Khera, MD, FACC
Nothing to disclose
Farzan Filsoufi, MD, FACC
Nothing to disclose
Stamatios Lerakis, MD, PhD, FACC, FAHA
Nothing to disclose
Gilbert Tang, MD, MSc, MBA, FACC [Moderator]
Physicain Proctor for Medtronic
Cardiac Anesthesiologist
Joseph Larese, MD

## Slide 3
Presentation: Chest pain, worsening NYHA Class III symptoms of heart failure for last few months
PMH: Hypertension, hyperlipidemia, non-obstructive CAD, HEpEF, s/p bio-prosthetic aortic valve replacement 2007 (23mm Perimount 2800Valve), peripheral venous stents RLE and LLE 2022 (on AC)
Medications: Lisinopril, Atorvastatin, Furosemide, Rivaroxaban
Labs: Hgb 7.6, PLT 235K, K 4.5, Cr 1.04, INR 1.6
EKG (6/24/22): Sinus rhythm, first degree AV block, PVC, RBBB
TTE (6/23/22): Severe bioprosthetic AS (PG/MG/PV: 85/51/4.6), mild to moderate MR, and mild TR. LVEF 50%.
TEE (6/24/22): Severe bio-prosthetic AS and moderate AI
Cath (6/22/22): Non-Obstructive coronary artery disease
Structural Heart Live Case # 48: RR, 80 y/o M

## Slide 4
Transthoracic Echocardiogram (TTE)
Doppler to show aortic stenosis

## Slide 5
Trans Esophageal Echocardiogram (TEE)

## Slide 6
Aortic Annulus
Max: 21.3 mm
Min: 20.7 mm
Mean: 21.0 mm
Perimeter = 65.9 mm
Area = 345.6 mm2
LVOT
Max: 30.1 mm
Min: 24.3 mm
Mean: 27.0 mm
Perimeter = 85.5 mm
Area = 570.7 mm2
CTA: Aortic annulus, LVOT

## Slide 7
CTA: STJ and SOV
STJ
Min 29.1 mm
Max 30.3 mm
Mean 29.7 mm
Sinus of Valsalva
RCC 32.7 mm
LCC 32.8 mm
NCC 33.1 mm

## Slide 8
CTA: Valve-To-Coronary (VTC) and Coronary Height
Coronary Heights
LM – 7.1 mm
RCA – 13.1 mm
VTC
Left VTC – 5.1 mm
Right VTC – 3.2 mm

## Slide 9
CTA: Vascular Access

## Slide 10
23 mm Perimount 2800 valve with bovine pericardial leaflets sutured “inside” the stent
Suggested ViV Evolut : 26mm
Valve in Valve positioning

## Slide 11
Summary of Case
Presentation: 80 year old M with NYHA Class III HF for 4-5 mths
TEE: Abnormal aortic bio-prosthesis with severe stenosis and moderate AI (PG/MG/PV 85/51/4.6, PHT 115 ms), EF 50%
STS risk mortality: 2.97%
Course: Patient was evaluated by Heart Team and determined to be high risk for surgical AVR due to medical comorbidities
Plan: TF ViV TAVR using 26mm Evolut FX in a 23mm Perimount 2800 valve via right percutaneous femoral artery after valve fracture with Sentinel Cerebral Embolic Protection Device

## Slide 12
Latest Issues in Transcatheter Structural Heart Interventions
SHD Trials from EuroPCR 2022:
- AMTRAC Registry
- Lyten Trial
- Optimize Pro Study
- Revasc-TAVI Trial
- STROke TAVI Study
- Jenavalve Trilogy TAVI

## Slide 14
Outcomes from the AMTRAC (Aortic+Mitral Transcatheter) Registry
Witberg et al., EuroPCR 2022; J Am Coll Cardiol Intv 2022;15;1266
* p<0.05

## Slide 16
Balloon- Versus Self-Expanding Valve Systems for Treating Small Failed Surgical Aortic Bioprostheses:
The LYTEN Trial

## Slide 17
LYTEN Trial
Rodés-Cabau J, EuroPCR 2022
Inclusion criteria:
  Patients with surgical aortic bioprosthetic failure defined as severe aortic stenosis and/or regurgitation approved for a valve-in-valve TAVI procedure by the Heart Team
  Small (≤23 mm, inner diameter ≤21 mm) stented surgical valves
Primary outcomes:
  Residual (maximal and mean) transvalvular gradient at 30 days
  Severe prosthesis-patient mismatch or moderate-severe aortic
regurgitation (VARC-2 definition) at 30 days
Secondary outcomes:
  Clinical endpoints at 30 days
  Hemodynamic measurements obtained by catheterization during the TAVI procedure (implemented at half of study enrollment)

## Slide 18
LYTEN Trial: Study Population Flowchart
Rodés-Cabau J, EuroPCR 2022
Patients accepted for
Valve-in-Valve TAVI and randomized to either BEV or SEV
(n=102)
BEV Group
Patients randomized to receive a SAPIEN 3/ULTRA valve
(n=49)
SEV Group
Patients randomized to receive an Evolut R/PRO/PRO+ valve
(n=53)
Patients who received intervention as randomized
(n=46)
Patients who received intervention as randomized
(n=52)
Patients with echocardiographic measurements (corelab)
(n=45)
Patients with echocardiographic measurements (corelab)
(n=52)
3 patients did not undergo the
valve-in-valve TAVI procedure
(1 patient died before the procedure; 2 patients were treated medically)
1 patient did not undergo the
valve-in-valve TAVI procedure
(1 patient died before the procedure)
1 patient withdraw informed consent before the 30 days follow-up

## Slide 19
LYTEN Trial: Baseline Characteristics
Rodés-Cabau J, EuroPCR 2022
 | BEV (n=49) | SEV (n=53) | P value
Clinical characteristics |  |  | 
Age, years | 79±6 | 80±6 | 0.30
Male | 59% | 47% | 0.22
STS, % | 5.9 (3.8-7.7) | 4.9 (3.7-7.0) | 0.75
Surgical valve prosthesis size, mm |  |  | 0.69
19 | 8% | 8% | 
21 | 43% | 49% | 
22 | 0% | 2% | 
23 | 49% | 42% | 
Surgical valve dysfunction |  |  | 0.89
Predominantly stenosis | 67% | 66% | 
Predominantly regurgitation | 33% | 34% | 
Echocardiographic characteristics |  |  | 
Left ventricular ejection fraction, % | 58±12 | 57±12 | 0.49
Mean aortic gradient, mm Hg | 39±16 | 35±14 | 0.23
Mean aortic gradient, mmHg (patients with stenosis dysfunction only) | 43±16 | 41±12 | 0.57
Maximal aortic gradient, mm Hg | 66±24 | 60±20 | 0.18
Maximal aortic gradient, mmHg (patients with stenosis dysfunction only) | 72±23 | 69±17 | 0.48
Effective valve area, cm2 | 0.93±0.36 | 0.95±0.36 | 0.88

## Slide 20
LYTEN Trial: Procedural Characteristics
Rodés-Cabau J, EuroPCR 2022
 | BEV (n=46) | SEV (n=52) | P value
Approach |  |  | 
Transfemoral | 91% | 87% | 0.46
Valve type |  |  | -
Sapien 3/ULTRA | 40/6 |  | 
Evolut R/PRO/PRO+ |  | 20/31/1 | 
Prothesis size, mm |  |  | <0.001
20 | 24% | 0 | 
23 | 76% | 65% | 
26 | 0 | 35% | 
Successful valve implantation | 100% | 100% | -
Balloon pre-dilation | 7% | 8% | 0.85
Balloon post-dilation | 20% | 23% | 0.67
Surgical ring fracture (before/after valve implantation) | 35% (4/10) | 13% (0/7) | 0.04
Valve embolization | 0 | 0 | -
Need for a second valve | 0 | 0 | -
Coronary obstruction | 2% | 0 | 0.47
Conversion to surgery | 0 | 0 | -
Procedural death | 0 | 0 | -

## Slide 21
LYTEN Trial: Maximal/Mean Transvalvular Gradient, Mean Residual Gradient >20 mmHg at 30-Day F/U
Rodés-Cabau J, EuroPCR 2022
There were no death or stroke in both groups

## Slide 22
LYTEN Trial: Severe PPM and AR
Rodés-Cabau J, EuroPCR 2022

## Slide 23
LYTEN Trial: Invasive vs Echocardiographic Measurements
Rodés-Cabau J, EuroPCR 2022
Discharge echocardiographic measurements:
median of 1 day post-procedure (n=55)

## Slide 24
LYTEN Trial: Conclusions
In patients with small failed surgical bioprostheses, ViV-TAVI was associated with an extremely low rate of periprocedural complications and 30-day adverse events irrespective of valve type
The Evolut R/PRO/PRO+ valve system provided improved valve hemodynamics (lower transvalvular residual gradient, tendency towards a lower severe PPM rate) compared to the SAPIEN 3/ULTRA valve as evaluated by Doppler-echocardiography
Invasive hemodynamics exhibited lower transvalvular gradients compared to echocardiographic measurements
There were no significant differences between valve types in invasive hemodynamic measurements obtained during the ViV- TAVI procedure

## Slide 25
Impact of a Standardized TAVI Technique and Care Pathway in the Optimize PRO Study

## Slide 26
Optimize PRO Study: Background
Safety and efficacy of utilizing standardized implant protocols and care pathways is limited in large prospective studies of TAVI.
Post procedure conduction disturbance and new permanent pacemaker implantation (PPI) results after TAVI have been variable.
Protocolizing pre-, peri- and post-procedure pathways may improve outcomes.
Grubb K, EuroPCR 2022

## Slide 27
Optimize PRO: Study Design
Grubb K, EuroPCR 2022
Non-randomized, prospective, post-market study
Conducted in the United States, Canada, Europe, Middle East, and Australia
AV Conduction Disturbance
Validate post procedural conduction disturbance management
No AV Conduction Disturbance
Procedural Efficiency & Collect
Economic Value Data
1 Year Follow-up
Symptomatic Severe AS
Primary Endpoint: Rate of all-cause mortality or all-stroke at 30 days
“Optimized” post- procedure care pathway
“Optimized” conduction disturbance management pathway
Secondary Endpoints:
Median days LOS
% of subjects with ≥ moderate AR at discharge
Rate of new PPI at 30 days
Medtronic Evolut PRO or Evolut Pro + device suitability inclusion criteria
Attempted Procedures
“Optimized” post- procedure care pathway
“Optimized” procedure

## Slide 28
Optimize PRO Study: Optimized TAVI Care Pathway with Evolut PRO/PRO+
Grubb K, EuroPCR 2022
Valve deployment using the cusp overlap technique
Pre-BAV not required
Avoid general anesthesia
Use transfemoral access only
Minimize central lines
Pre-Procedure
12-lead ECG
Early discharge plan with multi-disciplinary team
Screening checklist
Peri-Procedure
Post-Procedure
12-lead ECG within 2 Hours
If no pre-existing RBBB or ECG changes remove all lines*
Mobilize within 4-6 hours
Consider PACU or stepdown unit vs ICU
TTE and ECG prior to discharge
* Follow to conduction disturbance pathway if patients has pre-existing RBBB or ECG changes (PR and QRS increase ≥20 ms)

## Slide 29
Key Steps*
Initial deployment in the cusp overlap projection to estimate implant depth at the NCC
Deploy with the marker band positioned at mid-pigtail or higher
Assess depth in cusp overlap view
Roll LAO. Remove any remaining parallax. Estimated depth at the LCC
Redeployment in cusp overlap view, if applicable
Assess final implant depth on the NCC
Optimize PRO Study: Cusp Overlap Technique with Evolut PRO/PRO+
Grubb K, EuroPCR 2022
*Use of Lunderquist guidewire is highly recommended.

## Slide 30
Optimize PRO Study: Patient Flow
Grubb K, EuroPCR 2022
*10.4% screen failure rate for roll-in and main cohort
Roll-in*
N=104
30 Days
94.2%
(98/104)
Discharge
100%
(104/104)
Main Cohort*
N=400
Discharge
100%
(399/399)
Died: 1
Died: 2
Withdrew: 2
30 Days
93.2%
(368/395)

## Slide 31
Optimize PRO Study: Procedural Characteristics
Grubb K, EuroPCR 2022
 | Roll-In (N=104) | Main Cohort (N=400) | Combined (N=504)
Total time in procedure room (minutes) | 121.5 ± 34.6 | 112.8 ± 38.1 | 114.6 ± 37.6
Femoral access site | 100.0 | 100.0 | 100.0
Lunderquist extra-stiff guide wire | 61.5 | 86.7 | 81.5
Anesthesia type |  |  | 
Conscious sedation/MAC | 85.6 | 84.3 | 84.5
General anesthesia | 14.4 | 15.5 | 15.3
Bioprosthesis used |  |  | 
Evolut PRO | 9.6 | 8.0 | 8.3
Evolut PRO+ | 90.4 | 91.5 | 91.3
Pre-BAV | 46.2 | 59.5 | 56.7
Post-dilatation | 18.3 | 12.3 | 13.5
Embolic protection device used | 34.6 | 33.8 | 33.9
Implant depth, NCC (mm), core lab | 3.4 ± 2.7 | 3.1 ± 3.0 | 3.1 ± 2.9
Resheathing | 26.0 | 20.3 | 21.4
Full recapture used | 20.4 | 27.8 | 26.2

## Slide 32
Optimize PRO Study: Procedural Characteristics
Grubb K, EuroPCR 2022
 | Roll-In (N=104) | Main Cohort (N=400) | Combined (N=504)
Conduction Disturbance Group |  |  | 
No ECG changes | 51.0 | 64.0 | 61.3
Pre-existing RBBB & no ECG changes | 5.8 | 4.8 | 5.0
New onset LBBB | 28.8 | 18.3 | 20.4
ECG changes & pre-existing RBBB, LBBB, IVCD, or 1st degree AV block | 12.5 | 8.5 | 9.3
Peri-procedural HAVB | 1.9 | 4.5 | 4.0
Post procedure recovery used ICU | 26.0 | 27.6 | 27.2
Number of valves implanted |  |  | 
1 | 100.0 | 98.8 | 99.0
2 | 0.0 | 1.3 | 1.0
Length of stay (median days) | 1.0 | 1.0 | 1.0
Discharged with external Holter monitor | 25.0 | 21.1 | 21.9

## Slide 33
Optimize PRO: 30-Day Clinical Outcomes
Grubb K, EuroPCR 2022
Chart: 
| All-cause mortality or all stroke | All-cause mortality | All stroke | Disabling stroke
Main Cohort (n=400) | 3.8 | 0.8 | 3 | 0.7
Combined Cohort (n=504) | 3 | 0.6 | 2.4 | 0.6
%

## Slide 34
Optimize PRO Study: 30-Day Clinical Outcomes
Grubb K, EuroPCR 2022
Chart: 
| Bleeding | Major vasc compl | MI | Reintervn | Hosp readmission | CV hosp | PPM | New-onset LBBB
Roll-in (n=104) | 1 | 1.9 | 0 | 0 | 4.8 | 3.8 | 6.7 | 26.3
Main Cohort (n=400) | 1.8 | 2.8 | 1 | 0.3 | 10.1 | 6.1 | 9.8 | 21.3
Combined Cohort (n=504) | 1.6 | 2.6 | 0.8 | 0.2 | 9 | 5.6 | 9.2 | 22.3
%

## Slide 35
Optimize PRO Study: Compliance with Key Cusp Overlap Steps (Main Cohort)
Grubb K, EuroPCR 2022
Chart: 
| Valve Migration | Valve Embolization | Reintervention | 30-Day PPI Rate
Followed (n=221) | 0.9 | 0 | 0 | 8.1
Not Followed (n=78) | 2.6 | 1.3 | 1.3 | 11.5
%

## Slide 36
Optimize PRO Study: Hemodynamics
Grubb K, EuroPCR 2022
AV Mean Gradient | 389 | 380
Effective Orifice Area | 321 | 289
Echocardiographic outcomes assessed on the implanted population (N=398) and reviewed by a central core laboratory.
0.9±0.2
2.3±0.6
39.7±11.2
8.2±4.0
0.0
10.0
20.0
30.0
40.0
50.0
0.0
0.5
1.0
1.5
2.0
2.5
Baseline
Discharge
AV Mean Gradient (mmHg)
Effective orifice area (cm2)
Effective Orifice Area
AV Mean Gradient
# of evaluable echos

## Slide 37
Optimize PRO: AR at Discharge (Main Cohort)
Grubb K, EuroPCR 2022
78% None/Trace Regurgitation with Evolut PRO/PRO+
Chart: 
| Paravalvular (n=380) | Total (n=387)
None/Trace | 78.2 | 78
Mild* | 21.8 | 22
≥Moderate | 0 | 0
Percent of Patients
0.0
0.0
Echocardiographic outcomes assessed on the implanted population (N=398) and reviewed by a central core laboratory.
*1 patient with mild-moderate PVL in the 34 mm group.

## Slide 38
Optimize PRO Study: PVL at Discharge by
Valve Size
Grubb K, EuroPCR 2022
Chart: 
| 23 mm (n=4) | 26 mm (n=99) | 29 mm (n=196) | 34 mm (n=81)
None/Trace | 100 | 79.8 | 76 | 80.2
Mild | 0 | 20.2 | 24 | 19.8
3≥ Moderate | 0 | 0 | 0 | 0
Percent of Patients
Echocardiographic outcomes assessed on the implanted population (N=398) and reviewed by a central core laboratory.
*1 patient with mild-moderate PVL in the 34 mm group.

## Slide 39
Optimize PRO Study: Summary
Utilization of the Cusp Overlap Technique with an optimized care pathway provides excellent outcomes, low pacemaker implantation rate, expedited discharge and low rates of residual aortic regurgitation:
  30-day mortality (0.8%) and new pacemaker (9.8%)
    Compliance with key Cusp Overlap Technique steps resulted in numerically lower pacemaker implantation rate (8.1%)
  Next-day discharge (median LOS 1 day)
  0% moderate/severe PVL at discharge

## Slide 40
Management of Myocardial Revascularization in Patients with Stable Coronary Artery Disease Undergoing Transcatheter Aortic Valve Implantation
REVASC-TAVI

## Slide 41
REVASC-TAVI Trial: Background
Costa G, EuroPCR 2022
The benefit of myocardial revascularization in patients affected by severe AS and screened for SAVR or TAVI is currently unclear
AHA and ESC guidelines recommend to consider PCI in case of ≥70% stenosis in proximal coronary segments for patients undergoing TAVI (Class IIa, LoE C)
The possibility to schedule ad-hoc PCI procedures if needed, favours TAVI over SAVR+CABG

## Slide 42
REVASC-TAVI Trial: Primary and Secondary Outcomes
Costa G, EuroPCR 2022
Outcomes of patients undergoing TAVI with stable, significant CAD (≥70% or ≥50% in LM) at baseline according to the completeness of myocardial revascularization achieved
Primary outcome
All-cause death at 2 years
Co-primary composite outcome
All-cause death, stroke, MI or HF rehospitalization at 2 years
Secondary outcomes
Stroke, MI, HF rehospitalization and unplanned PCI at 2 years

## Slide 43
REVASC-TAVI Trial: Study Design
Costa G, EuroPCR 2022
Patients with available data about baseline CAD and PCI performed (n=2025)
Patients undergoing TAVI with significant, stable CAD at baseline (n=2402)
Complete revascularization
(n=1310)
Incomplete revascularization
(n=715)
No follow-up data available (n=231)
675 pairs of patients compared
through 1:1 PS matching
No data about the completeness of myocardial revascularization (n=146)

## Slide 44
REVASC-TAVI Trial: CAD and PCI Characteristics
Costa G, EuroPCR 2022
CAD and PCI characteristics | Overall (n=1314) | Complete revascularization (n=657) | Incomplete revascularization (n=657) | p-value
Diseased vessels |  |  |  | <0.001
1, n (%) | 668 (50.8) | 434 (66.1) | 234 (35.6) | 
2, n (%) | 382 (29.1) | 150 (22.8) | 232 (35.3) | 
≥3, n (%) | 264 (20.1) | 73 (11.1) | 191 (29.1) | 
Multivessel CAD, n (%) | 646 (49.2) | 223 (33.9) | 423 (64.4) | <0.001
Proximal CAD, n (%) | 834 (63.5) | 408 (62.1) | 426 (64.8) | 0.330
LM/proximal LAD CAD, n (%) | 485 (36.9) | 240 (36.5) | 245 (37.3) | 0.819
PCI, n (%) | 944 (71.8) | 657 (100.0) | 287 (43.7) | <0.01
PCI timing, n (%) |  |  |  | 0.027
Staged before TAVI | 579 (61.3) | 408 (62.1) | 171 (59.6) | 
Staged after TAVI | 102 (10.8) | 73 (11.1) | 29 (10.1) | 
Concomitant to TAVI, before valve | 190 (20.1) | 124 (18.9) | 66 (23.0) | 
Concomitant to TAVI, after valve | 59 (6.2) | 47 (7.2) | 12 (4.2) | 
Unplanned PCI | 3 (0.3) | 1 (0.2) | 2 (0.7) | 
PCI in proximal vessels, n (%) | 580 (61.4) | 392 (59.7) | 188 (65.5) | 0.095
Multivessel PCI, n (%) | 246 (26.1) | 148 (22.5) | 98 (34.2) | <0.01
LM/proximal LAD PCI, n (%) | 339 (35.9) | 222 (33.8) | 117 (40.8) | 0.046

## Slide 45
REVASC-TAVI Trial: Procedural Outcomes
 | Overall (n=1314) | Complete revascularization (n=657) | Incomplete revascularization (n=657) | p-value
Vascular access, n (%) |  |  |  | 0.080
Trans-femoral | 1238 (94.2) | 608 (92.5) | 630 (95.9) | 
Others | 66 (5.0) | 43 (6.6) | 23 (3.5) | 
SAT protection, n (%) | 47/1236 (3.8) | 25/610 (4.1) | 22/626 (3.5) | 0.656
TAV type, n (%) |  |  |  | -
SAPIEN 3/3 Ultra | 494 (37.6) | 267 (40.6) | 227 (34.6) | 
SAPIEN XT | 16 (1.2) | 6 (0.9) | 10 (1.5) | 
Evolut R/PRO/PRO+ | 493 (37.5) | 234 (35.6) | 259 (39.4) | 
CoreValve | 47 (3.6) | 24 (3.6) | 23 (3.5) | 
Portico | 69 (5.2) | 36 (5.5) | 33 (5.0) | 
Acurate NEO/NEO 2 | 131 (10.0) | 67 (10.2) | 64 (9.8) | 
Others | 57 (4.4) | 21 (3.2) | 36 (5.7) | 
Local anaesthesia, n (%) | 1103/1304 (84.6) | 558/653 (85.5) | 545/651 (83.7) | 0.186
Post dilatation, n (%) | 261/1197 (21.8) | 121/572 (21.1) | 140/625 (22.5) | 0.576
Need 2nd TAV, n (%) | 22/1294 (1.7) | 10/663 (1.5) | 12/631 (1.9) | 0.830
Costa G, EuroPCR 2022

## Slide 46
REVASC-TAVI Trial: Primary Outcomes
Complete Revasc vs Incomplete Revasc
Costa G, EuroPCR 2022
Primary Outcome
(All-cause death)
Co-Primary Endpoint
(All-cause death, stroke, MI, or HF rehosp)

## Slide 47
Costa G, EuroPCR 2022
REVASC-TAVI Trial: Primary Outcomes
Complete Revasc vs Incomplete Revasc w/ PCI vs Incomplete Revasc w/o PCI
Costa G, EuroPCR 2022
Primary Outcome
(All-cause death)
Co-Primary Endpoint
(All-cause death, stroke, MI, or HF rehosp)

## Slide 48
REVASC-TAVI Trial: Subgroup Analyses of the Primary Endpoint Outcome
Costa G, EuroPCR 2022

## Slide 49
REVASC-TAVI Trial: Summary
Costa G, EuroPCR 2022
This was the largest analysis evaluating the impact of myocardial revascularization in patients undergoing TAVI
The completeness of myocardial revascularization achieved in patients scheduled for TAVI did not impact on their prognosis at 2 years, regardless the clinical subset and the quote of myocardium at risk
Pending the validation of lesion functional assessment in the setting of severe AS, leaving angiographically significant, stable CAD untreated in TAVI patients is reasonable and gives the chance to reassess the need of revascularization thereafter
Coronary re-access difficulties after TAVI must be considered

## Slide 50
Management and Outcomes of Stroke Complicating Transcatheter Aortic Valve Implantation
The Acute STROke complicating TAVI collaboration

## Slide 51
We aimed to explore the characteristics of acute stroke complicating TAVI and to describe the incidence and outcomes of emergent interventions to treat acute stroke complicating TAVI.
STROke TAVI Study: Objective
Levi A, EuroPCR 2022

## Slide 52
STROke TAVI Study Design
Levi A, EuroPCR 2022
Consecutive periprocedural stroke cases were collected from 14 centers in a dedicated multinational database: ASTRO-TAVI
Stroke severity was assessed using the National Institute of Health Stroke Scale (NIHSS).
Prespecified primary outcomes were 1- year all cause death, and neurologic disability status at 60-90 days according to the modified rankin score (mRS).

## Slide 53
STROke TAVI Study: TAVI to Stroke
Time Interval
Levi A, EuroPCR 2022

## Slide 54
STROke TAVI Study: Mortality with Respect
to Stroke Severity
Levi A, EuroPCR 2022

## Slide 55
STROke TAVI Study: Moderate and Severe Stroke – Baseline Characteristics
Levi A, EuroPCR 2022
 | All n = 145 | Conservative n = 109 | Neurointervention n = 36 | P value
Age, mean (sd) | 81.3 (9.2) | 81.3 (10) | 81.5 (6.2) | 0.87
Male gender, n(%) | 51 | 46.8 | 63.9 | 0.09
Baseline NYHA, mean(sd) | 2.8 (0.6) | 2.8 (0.6) | 2.9 (0.7) | 0.55
Creatinine (g/dL), mean(sd) | 1.4 (1.2) | 1.4 (1.3) | 1.3 (0.5) | 0.28
COPD, n(%) | 17.2 | 18.3 | 13.9 | 0.62
Diabetes mellitus, n(%) | 31.7 | 30.3 | 36.1 | 0.6
Hypertension, n(%) | 76.6 | 75.7 | 79.4 | 0.82
Peak gradient, mean(sd) | 70.8 (27) | 68.6 (26.4) | 77.3 (28.1) | 0.12
Mean gradient, mean(sd) | 42.8 (17.6) | 41.2 (17.1) | 47.5 (18.7) | 0.08
Valve area cm2, mean(sd) | 0.7 (0.2) | 0.7 (0.2) | 0.7 (0.2) | 0.24
STS score, mean(sd) | 5.8 (4.6) | 6 (4.8) | 4.8 (4) | 0.16

## Slide 56
STROke TAVI Study: Moderate and Severe Stroke – Procedural Characteristics
Levi A, EuroPCR 2022
 | All n = 145 | Conservative n = 109 | Neurointervention n = 36 | P value
General anesthesia, n(%) | 37.3 | 43.5 | 15.4 | 0.01
Embolic protective d, n(%) | 6.2 | 5.6 | 8.3 | 0.69
Self expandable d, n(%) | 68.3 | 67.9 | 69.4 | 1
Alternative access, n(%) | 21.5 | 25.9 | 8.3 | 0.03

## Slide 57
STROke TAVI Study: Mild to Severe Stroke Clinical Outcome
Levi A, EuroPCR 2022

## Slide 58
STROke TAVI Study: Stroke Disability at 90 Days Grouped by Stroke Severity
Levi A, EuroPCR 2022
Independent survival at 90 days - neurointervetnion versus conservative therapy,
adjusted for NIHSS group and STS score: Odds Ratio 2.9 (95% CI 1.2-6.9, p=0.02)

## Slide 59
STROke TAVI Study Summary
Levi A, EuroPCR 2022
Stroke after TAVI is a serious complication and frequently occurs in 0-2 days; mortality is high and is directly related to stroke severity
With the adoption of TAVI in a wider specrum of patients, we should not only focus on stroke prevention but also on aggressive medical and mechanical stroke treatment
Higher rates of independent survival could be achieved if neuro-intervention is applied rapidly in an appropriate indication
We herein demonstrate, for the first time, the potential benefit of neuro-intervention to treat stroke after TAVI

## Slide 60
TAVR STROKE Protocol at MSH

## Slide 62
The Jenavalve Trilogy TAVI System for Treatment of Aortic Regurgitation:
Worldwide First Results in a Multicenter Real-World Cohort

## Slide 63
Jenavalve Trilogy TAVI System
Tamm A, EuroPCR 2022
The Trilogy TAVI System features unique locators that align the THV with the native cusps of the valve and ensures anatomically correct alignment
The locators “clip” onto the native leaflets, enabling anchoring in pure AR patients with non-calcified valves.
Jenavalve Trilogy Valve
Jenavalve Trilogy valve after implantation with perfect position and no paravalvular regurgitation
Prosthesis with locators spread during implantation, seating locators in the sinuses

## Slide 64
Jenavalve Trilogy Endpoints
Tamm A, EuroPCR 2022
Primary Efficacy Endpoint:
Technical success with mean gradient < 20mmHg and reduction of AR grade by >1.
Combined Primary Safety Endpoint:
Major adverse events (death, myocardial infarction, cardiothoracic surgery, stroke) at discharge.

## Slide 65
Jenavalve Trilogy: Baseline Characteristics
Tamm A, EuroPCR 2022
All Patients presented with moderate-severe or severe AR
Mean patient age was 77 years, with 40% female
Mean EuroSCORE II was 7.1%
71% of the patients were in functional NYHA class III or IV
13 patients (29%) had previous cardiac surgery
58% of patients with LVEF ≤50%
N = 451 | 
Age (years) | 76.8 (9.52)
Sex (female) | 18 / 45 (40%)
EuroSCORE II | 7.08 (9.00)
NYHA III/IV | 32/45 (71%)
BMI (kg/m2) | 26.86 (5.70)
Atrial Fibrillation | 26 / 45 (58%)
COPD | 4 / 45 (8.9%)
Arterial hypertension | 42 / 45 (93%)
Diabetes mellitus | 10 / 45 (22%)
Previous cardiac surgery | 13 / 45 (29%)
Previous PCI | 13 / 35 (37%)
Previous pacemaker | 6 / 45 (13%)
Previous Stroke | 5 / 45 (11%)
Prior right bundle branch block | 1 / 45 (2.2%)
Prior left bundle branch block | 6 / 45 (13%)
LVEF ≤50% | 26/45 (58%)

## Slide 66
Jenavalve Trilogy: Procedural Characteristics
Tamm A, EuroPCR 2022
All cases were performed via transfemoral access
82% of cases performed under conscious sedation
Post-dilatation was performed in 2 cases
Median procedure time of 77 mins
N = 451 | 
Valve Size | 
23 mm | 4 / 45 (8.9%)
25 mm | 14 / 45 (31%)
27 mm | 27 / 45 (60%)
Conscious sedation | 37 / 45 (82%)
Pre-dilatation | 0 / 45 (0%)
Post-dilatation | 2 / 45 (4.4%)
Procedure duration (min) | 76.49 (20.17)
Contrast (ml) | 180.58 (77.59)
Fluoroscopy time (min) | 19.20 (5.87)

## Slide 67
Jenavalve Trilogy: Clinical Results
Tamm A, EuroPCR 2022
N = 451 | 
Technical success | 45 / 45 (100%)
Conversion to open surgery | 0 / 45 (0%)
Bleeding complications | 
minor bleeding | 3 / 45 (6.7%)
major or life-threatening bleeding | 0 / 45 (0%)
Major vascular complication | 1 / 45 (2.2%)
AKI – stage 2 or 3 | 0 / 45 (0%)
Stroke | 0 / 45 (0%)
In-hospital mortality | 0 / 45 (0%)
Mean aortic valve gradient, mmHg (discharge) | 4.04 (1.64)
Aortic valve area, cm2 (discharge) | 2.62 (0.64)
New pacemaker | 9 / 39 (23%)
Chart: 
| N=45
None | 55.5
Trace | 35.5
Mild | 9
≥ Moderate | 0
Paravalvular Regurgitation
91% None or Trace

## Slide 68
Jenavalve Trilogy: Summary
Treatment of aortic regurgitation with TAVI is challenging and is associated with poorer outcomes
This is an analysis of the first, real-world, commercial experience of the recently approved Jenavalve Trilogy TAVI System in a multi-center cohort
45 consecutive patients with aortic regurgitation from 6 German centers were included in this study
This study demonstrated excellent clinical outcomes, meeting both the primary safety and efficacy endpoints with no major adverse events and no moderate or severe AR at discharge
The Jenavalve Trilogy System is the only THV in the world approved for use to treat both AS and AR. Further studies with expanded cohort of AI/AS pts will be needed to prove its safety and efficacy.
Tamm A, EuroPCR 2022

## Slide 69
Take Home Messages
SHD TAVI/TAVR Trials from EuroPCR 2022
Peri-procedural and mortality outcomes were higher after SEV at BEV dominant centers while no difference in 2 valve outcomes at SEV dominant centers. This is important when we compares 2 valves.
ViV TAVR for surgical valves <23mm, with SEV had better hemodynamics and lower PPM compared to BEV. Hence SEV should be preferred in this setting, if these data translates into better clinical outcomes.
Dedicated protocolized strategy for SEV deployment has shown to have superior outcomes vs historical data and should be routinely practiced.
Coronary revascularization in pts with severe AS undergoing TAVI has not shown to impact survival and other clinical outcomes at 2 yrs. Hence PCI of significant coronary lesions is not routinely indicated. COMPLETE TAVR trial will give the final answer.
Stroke after TAVI has graded mortality depending on the severity. Aggressive management by neurointervention of these cases can improve subsequent outcomes and mortality
Jenavalve Trilogy TAVI system has shown optimal and safety outcomes in pts with pure severe AR. Jenavlave is poised to expand the TAVI horizon.

## Slide 70: Question # 1
Following are the recommended components of Optimize PPRO study for TAVR in AS pts except:
  Valve deployment using cusp overlap
  If no heart blocks, then remove all central lines
  Mobilize in 4-6 hrs
  Pre-BAV is essential in all cases
Correct answer: D

## Slide 71: Question # 2
Following statements is false regarding the results of REVASC-TAVI:
  All cause death were similar in gps with or without revascularization
  All cause death, stroke, MI or HF rehosp were similar in 2 gps
  Group with Incomplete revascularization with PCI has worse outcomes
  Outcomes were better with PCI in MV/LM CAD vs no PCI
Correct answer: C

## Slide 72: Question # 3
Following are the results of the LYTEN trial comparing SEV vs BEV in small surgical valves except:
  A. SEV had better clinical outcomes at 30-days vs BEV gp
  B. SEV gp had lower maximal residual gradient vs BEV gp
  C. SEV gp has lower severe PPM vs BEV gp
  D. SEV gp has lower incidence of MG >20 mmHg vs BEV gp
Correct answer: A